## Slide 1: DYNAMAP Project: Procedure for Noise Mapping Updating in Urban Area
G. Zambon, A. Bisceglie, R. Benocci, M. Smiraglia, H.E. Roman
Dipartimento di Scienze dell’Ambiente e del Territorio e di Scienze della Terra,
Università di Milano-Bicocca, Piazza della Scienza 1, 20126 Milano, Italy
INTER-NOISE 2017
46TH INTERNATIONAL CONGRESS AND EXPOSITION
ON NOISE CONTROL ENGINEERING
HONG KONG
27 - 30 AUGUST, 2017

## Slide 2
CONTENT:
What is DYNAMAP
Where it is implemented
Basic Idea: Interpolation
Non-Acoustic Parameter
Pilot Area of DYNAMAP
The Six Groups: Noise Maps
Initialization - Updating of DYNAMAP
7.1 Treatement of Noise Signal and Leq variations from each Station
7.2 Starting Operation of Dynamap from 4 stations in each group
7.3 The group acceptance interval: Elimination of anomalous events
  7.4 Operation using the Clustering of the 24 recording stations
  7.5 Leq at time t for arbitrary receiver point a.
  8. CONCLUSIONS.

## Slide 3
DYNAMAP: Goals
Generate Real-Time
Dynamic Traffic Noise Maps
within a Large Urban Area
using few Monitoring Noise Stations.
Each Noise Map represents a group of road stretches,
displaying similar Acoustic Equivalent Levels, Leq.

## Slide 4
2. The Nine Urban Areas of Milan City
Urban Zone 9
(Pilot Area)

## Slide 5
3. Modeling Noise in a Large Urban Area:
Basic Observations on Data of 93 noise stations
The hourly Traffic Noise from the 93 monitoring stations analized: standard clustering techniques.
The TWO-cluster results: Cluster 1 and 2.
C1 represents low traffic roads (N=56)
C2 represents high traffic roads (N=37)
Figure displays the mean normalized acoustic equivalent levels [dB] for each cluster =1,2 as a function of the hour of the day.
The Idea is to interpolate between behaviors of C1 and C2 for arbitrary road.

## Slide 6
Distribution functions P1(x) and P2(x) of x = log(TT) on Noise Clusters 1 and 2, respectively. (N=93)
The continuous lines represent logarithmic fits to the
actual histograms using the cumulative distribution
functions, used to determine β1,2 accurately.
  TT = Total daily traffic flow rate
  The non-acoustic parameter x = Log(TT)
  The distribution functions P1(x) and P2(x)
  of x on each cluster.
  The probability that x belongs to Cluster 1
  β1(x) = P1(x) / (P1(x)+ P2(x))
  and to Cluster 2
  β2(x) = P2(x) / (P1(x)+ P2(x))
Interpolation scheme:
The non-acoustic parameter x.
x
P(x)

## Slide 7
5. DYNAMAP Pilot Area: The Urban Zone 9 of Milan City
Monitoring Traffic Noise by
means of 24 Noise Stations
Noise Stations
Is divided into SIX Groups
According to Non-Acoustic
Parameter X.
FOUR stations per Group.

## Slide 8
X 0.0 – 3.3 3.3 – 3.5 3.5 – 3.9 3.9 – 4.2 4.2 – 4.5 4.5 – 5.2
β1 0.99 0.81 0.63 0.50 0.41 0.16
β2 0.01 0.19 0.37 0.50 0.59 0.84
6. The Six Groups (Acoustic Maps, X = log(TT))
- Zone 9 of Milan City -
X
Mean values of β1 and β2 for each group g.

## Slide 9
=Leqτ,M(g,j)(measured) - Leqref,M(g,j)(calculated)
7.1 Treatement of Noise Signal and Leq variations from each Station
Each station j records a noise signal at 30 ms resolution.
Signal integration after filtering anomalous events into 1 sec Leq.
Further integration to get Leq
Operator gets 24 Leq values every min, and calculate the variations:
( j=1,2,3,4 is station index j inside group g ). The time intervals are distributed according to:
τ = 5 min in (7:00-21:00), τ = 15 min in (21:00-1:00), τ = 60 min in (1:00-7:00)
(1)
7. Initialization-Updating of DYNAMAP

## Slide 10
7.2 Starting Operation of Dynamap from 4 stations in each group:
=
Once all the values are obtained, the six acoustic maps
can be updated corresponding to each group by averaging the
variationsin Eq. (1) over the four values j in each group, as
=(1,2,3,4,5,6) and time interval .
7. Initialization-Updating of DYNAMAP
(2)

## Slide 11
7.3 The group acceptance interval: Elimination of anomalous events
The variations generated from the (g,j)th station must remain bounded
within the group acceptance interval
[, ]
where is the interquartile range obtained as the difference between
the 75th (t)) and 25th () percentiles calculated at the same time t
(of duration time τ) of the day for all .
7. Initialization-Updating of DYNAMAP

## Slide 12
Boxplot and a probability density function (PDF)
of a Normal N(0,σ) distribution.

## Slide 13
  7.4 Operation using the Clustering of the 24 recording stations:
=
=
Once compositions of Cluster 1 and 2 have been found (N1 stations in Cluster 1, k1=(1,…,N1), and N2 in Cluster 2, k2=(1,…,N2), such that N1+N2 = 24), we rearrange the variations obtained from Eq. (1) to get and within each cluster C1 and C2. The mean variations, and , for each cluster are,
7. Initialization-Updating of DYNAMAP

## Slide 14
Here, the allowed ranges of variation of (, are determined similarly as before,
[, ]
calculated for all stations (k1,k2) within each Cluster C1 and C2, respectively.
7. Initialization-Updating of DYNAMAP
=1() + 2()
The mean variation associated to each group g is,
(3)

## Slide 15
  7.5 Leq at time t for arbitrary receiver point a:
7. Initialization-Updating of DYNAMAP
The absolute at time t for an arbitrary receiver point a can be obtained from the measured values of (Eq. (2) or Eq. (3)). First, we need the value of Leqref(g,a) at the
receiver point a due to the noise produced by roads in the group g, which is provided by
the calculated (CADNA) acoustic map. The absolute at location a at time t=nτ can
then be estimated by,

## Slide 16
8. CONCLUSIONS
We have discussed a procedure for starting and implementing the six acoustic maps (one for each group g) of Dynamap for the Zone 9 of the City of Milan.
This procedure considers three time intervals during the day:
Th=(07:00 - 21:00), (21:00 - 01:00), (01:00 - 07:00),
for the three discretization times τ= (5, 15, 60) min, respectively.
We have presented two methods for evaluating the variations [dB]:
In the first one, the average of variations is performed over the four stations within each group g, Eq.(2).
In the second method, we use the corresponding values 1() and 2() for each group g and Eq. (3).
Finally, we have presented the general formula for obtaining the absolute at time t for the update time τ at an arbitrary receiver point a.

## Slide 17
THANK YOU VERY MUCH
FOR YOUR ATTENTION